## Slide 1: Target Tracking by a Quadrotor using Proximity Sensor Fusion
Varun Nayak[1], Raksha Rao Karaya[2]
[1]: Department of Mechanical Engineering, Birla Institute of Technology and Science, Pilani – K K Birla Goa Campus
[2]: Department of Aerospace Engineering, Indian Institute of Technology Madras

## Slide 2: Background
Summer research work at the Department of Aerospace Engineering at IIT Madras in the Flight Dynamics and Control Group
Lab focused on Multirotor Dynamics and Control.
To develop a low-cost and computationally efficient system on a quadrotor to be able to detect and “follow” a moving object.
Contribute to the lab’s objective of improving autonomy and efficiency of multirotor systems.

## Slide 3: Literature Review
Camera and Machine Vision
  Computational Cost – Ground Station Processing
  Fails in visually-degraded environments
Time of Flight Sensors
  LiDaR – Payload Limitations; Open-ended environments
Similar work using a combination of light-weight T-o-F sensors
  Gageik et al (2015): Combines US and IR sensor but does not demonstrate object tracking

## Slide 4: Objective
To detect and follow a solid object in front of a quadrotor by regulating its distance from it.
  Develop this system on top of a low-level attitude controller of the quadrotor.
  Make best use of available proximity sensors to generate the desired control signal – Filtering and Sensor Fusion
  Implementation and experimental verification.
Advantages: Computationally cheap, low-cost, readily available components, independent of light conditions, small payload

## Slide 5: Sensors
Proximity sensors that operate using ultrasonic signals.
Selection criteria – range, response for nature of surface, noise characteristics, measuring angle.
Validated from visualizing raw-data.

## Slide 6: Fully-assembled system
Flight Controller
+
Companion Board
Proximity Sensors

## Slide 7: Estimation: Filtering
Important to ensure a smooth and reliable stream of proximity data as the output of the filter will drive the high-level controller of the quadrotors.
Exponential Smoothening.
Digital Filter.
Noise Based (Gaussian) Filter.

## Slide 8: Estimation: Noise-based (Gaussian) filter

## Slide 9: Estimation: Sensor Fusion using Sigmoid Function

## Slide 10: System Dynamics
Ground frame and frame fixed on moving object
Balancing the force in the vertical and horizontal directions
Vertical direction: Static

## Slide 11: Simulink Model of Closed-Loop Dynamics
Objective: To estimate the PID gains required to perform successful trajectory tracking

## Slide 12: Simulation Results
Simulation of the PID Controller on MATLAB: Shows errors of less than 3 cm.
Sinusoidal Movement
Linear Movement

## Slide 13: Hardware Implementation

## Slide 14: Algorithm Flow Chart (implemented on the companion board-Arduino)
Three Modes:
  Manual
  Alt Hold
  “Follow Me”
Control law for Pitch Reference input signal that would translate the quadrotor.

## Slide 15: Results
Errors of the order of 20cm. However, tracking is performed successfully for the intended application.

## Slide 16: Conclusion
Cheap (developed under $150) and effective method to detect and track moving references in space using ultrasonic sensors. Such systems can be used for localization and tracking applications.
Limitation 1: The sensor readings were affected by the pitch angle because of the fixed mounting
Limitation 2 : Interference between the sensors added to noise

## Slide 17: Thank you
Questions?